## Slide 1
Prof. Yajun Ha
EE 216 Reconfigurable Computing
ShanghaiTech University
Shanghai, China
Topic 3 FPGA Architectures
Notes: 1

## Slide 2: The 2nd Major FPGA Book to Read
Reconfigurable Computing: The Theory and Practice of FPGA-Based Computation,
By Scott Hauk and Andre Dehon, Morgan Kaufmann, 2008, ISBN-10: 0123705223

## Slide 3
Reconfigurable Architectures
Coarse Grain Reconfigurable Architectures
FPGA Logic Blocks
FPGA Interconnects
Architecture Evaluation

## Slide 4: Granularity of Reconfigurable Architectures
Functional Block
I/O Block
Routing Network
Functional blocks are built by LUTs or ALUs?
Wires are organized by individually or by bus or channels?
Notes: What are the major factors to be considered for the design of an embedded SoC?
The most important factor is TTM. In other words, you must design and sell it faster than others or you lose. I’ll explain this in the following slides.
The technology advances rapidly and there are lots of challenges.
Leveraging on the advances in the technology, we must be able to satisfy the ever-increasing performance need.
Power consumption is another important issue.
Reliability, ...
Cost is still an important issue. Chip area is the most concern in our case.

## Slide 5: Reconfigurable Architecture Space
Fine Grain Reconfigurable Architectures (FPGA)
  Array of bit level function blocks (LUTs)
  Implement bit manipulation tasks without wasting resources
  Numerous PEs to implement a basic computation
  Slower clock rate and larger area to implement word-level computations
Coarse Grain Reconfigurable Architectures
  Array of coarse grain ALU or multipliers
  Interconnects are coarse grain as well, e.g., bus based.
  Not suitable for bit level operations.
  Compilers are hard to develop as multi-core processors.

## Slide 6: Coarse Grain RA
rDPA: reconfigurable Data Path Array
Function Units with programmable interconnects
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU

## Slide 7
rDPA: reconfigurable Data Path Array
Function Units with programmable interconnects
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Coarse Grain RA

## Slide 8: Example: PipeRench
Coarse granularity
Higher level programming
Reference papers
  PipeRench: A Coprocessor for Streaming Multimedia Acceleration (ISCA 1999): http://www.cs.cmu.edu/~mihaib/research/isca99.pdf
  PipeRench Implementation of the Instruction Path Coprocessor (Micro 2000): http://class.ee.iastate.edu/cpre583/papers/piperench_Micro_2000.pdf

## Slide 9: Example: PipeRench
Interconnect
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
Interconnect
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
8-bit ALU
Reg file
PE
Global bus

## Slide 10
Reconfigurable Architectures
Coarse Grain Reconfigurable Architectures
FPGA Logic Blocks
FPGA Interconnects
Architecture Evaluation

## Slide 11: FPGA Logic Blocks
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Configurable Logic Block

## Slide 12: FPGA Functional Blocks
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Configurable Logic Block

## Slide 13: FPGA Logic Blocks
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Configurable Logic Block

## Slide 14: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
0000
0001
1110
1111
ABCD Z
B
C
D
A
0000
0001
1110
1111
ABCD Z
0
0
0
1
AND
Z
A
B
C
D
0000
0001
1110
1111
ABCD Z
0
1
1
1
OR
Z
A
B
C
D
X000
X001
X010
X101
X110
X111
ABCD Z
0
1
0
0
1
1
B
2:1
Mux
C
D
Z
1
0

## Slide 15: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
B
C
D
A
How many 4-LUTs needed
to OR 32-bits
32
1
4
LUT
4
LUT
4
LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT

## Slide 16: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
B
C
D
A
How many 4-LUTs needed
to AND 2-bits with the 32-bit OR
32
1
4
LUT
4
LUT
4
LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT
4 LUT

## Slide 17: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
B
C
D
A
How could one build a 4-LUT?
0
0
0
0
0
1
1x16
Memory
16:1
Mux
4
ABCD
Z

## Slide 18: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
B
C
D
A
How many different 4 input functions can a 4-LUT implement?
0
0
0
0
0
1
1x16
Memory
16:1
Mux
4
ABCD
Z
216 = 65536

## Slide 19: Computational Fabric - LUT
4-LUT
Z
LUT = Look up Table
B
C
D
A
How many different N input functions can a N-LUT implement?
0
0
0
0
0
1
1x2N
Memory
16:1
Mux
N
ABCD
Z
216 =224=65536
N = 4
= 22N

## Slide 20: Computational Fabric - DFF
LUTs are fine for implementing any arbitrary combinational logic (output is ONLY a function of its inputs) function. But what about sequential logic (output is a function of input AND previous state information)?
4-LUT
Z
B
C
D
A
Need Memory!!!

## Slide 21: Computational Fabric - DFF
4-LUT
Z(t)
B
C
D
A
DFF
Z(t+1)
1/0
0/0
1
11
110
1101
1/0
0/0
1/1
0/0
Start
1/0
Input/output
Detect the pattern “1101”
DFF = D Flip Flop

## Slide 22: Computational Fabric - DFF
4-LUT
Z(t)
B
C
D
A
DFF
Z(t+1)
Increase circuit performance (pipelining)
4-LUT
B
C
D
A
DFF
4-LUT
DFF
4-LUT
DFF
4-LUT
DFF
4 LUT delays
per output
4-LUT
B
C
D
A
DFF
4-LUT
DFF
4-LUT
DFF
4-LUT
DFF
1 DFF delay
per output
DFF = D Flip Flop

## Slide 23: One Logic Element
F
4-LUT
Z(t)
B
C
D
A
DFF
Z(t+1)

## Slide 24: FPGA Functional Block
LE
LE
LE
Local
Inter-
connect
…..
Functional Block
Inputs
Functional Block
Outputs
Functional Block Internals
FPGAs use the Look-Up Table (LUT) type of functional block. Such a functional block is normally made of one or several logic elements (LE). They differentiate from each other mainly in terms of the input size of a LE and the number of LEs in a functional block. State-of-the-art FPGAs normally use 4-input LEs.

## Slide 25: Simplified FPGA Architecture
Functional Block
I/O Block
Routing Network
All the three FPGA components can be re-programmed with configurations to implement application-specific digital circuits.
For example, each functional block can be programmed to implement a small amount of digital logic of a design; the routing network can be programmed to implement the design specific interconnection pattern; I/O blocks can be programmed to implement the input and output ports according to design requirements.
Notes: What are the major factors to be considered for the design of an embedded SoC?
The most important factor is TTM. In other words, you must design and sell it faster than others or you lose. I’ll explain this in the following slides.
The technology advances rapidly and there are lots of challenges.
Leveraging on the advances in the technology, we must be able to satisfy the ever-increasing performance need.
Power consumption is another important issue.
Reliability, ...
Cost is still an important issue. Chip area is the most concern in our case.

## Slide 26: Contemporary FPGA Architecture
Notes: What are the major factors to be considered for the design of an embedded SoC?
The most important factor is TTM. In other words, you must design and sell it faster than others or you lose. I’ll explain this in the following slides.
The technology advances rapidly and there are lots of challenges.
Leveraging on the advances in the technology, we must be able to satisfy the ever-increasing performance need.
Power consumption is another important issue.
Reliability, ...
Cost is still an important issue. Chip area is the most concern in our case.

## Slide 27: Optimized Resources: Dedicated Logic
LUTs + DFFs can implement any arbitrary digital
logic. But not optimally (ASICs give make much
better use of silicon area for Power, Speed, routing
resources)
Arithmetic
  Add, Multiply
On chip memory
System on chip building blocks
  Processor, PCI-express, Gigabit Ethernet, ADC, etc.

## Slide 28: Optimized Resources: Dedicated Logic
Carry Look Ahead
c4
Carry in
Carry out
6-LUT
6-LUT
6-LUT
A3
B3
A2
B2
A1
B1
Sum 3
Sum 2
Sum 1
G1
P1
Sum
1
CLB
P2
Carry
2
G2
CLB
Sum
2
A1
B1
A1
B1
A1
B1
Carry1
Carry1
Carry1
A2
B2
Fast Addition
Two output LUT
generate propagate
logic
Dedicated routing
resources

## Slide 29: Optimized Resources: Dedicated Logic
Dedicated memory block
Embedded Memory
8
12
18 Kbits, 550 MHz

## Slide 30: Optimized Resources: Dedicated Logic
Multiplication
Type | # LUTs | Latency | Speed
LUT | ~400 | 5 clks | 380 MHz
Dedicated 18x18 Multiplier | 0 | 3 clks | 450 MHz
Virtex-5 (6-LUTs)
18x18 multiply
Very rough estimate of Silicon area comparison
(assuming SX95 andLX110 have about the same die size)
6-LUT
6-LUT
6-LUT
6-LUT
18x18
Multiplier
In other word you can replace
one LUT-based 18x18 multiplier
With 100 dedicated 18x18
Multipliers!!!

## Slide 31: Optimized Resources: Dedicated Logic
Processors
ARM hard-core
MicroBlaze soft-core
Quad A53 cores
Clock up to 1.5G
Superscalar
Zynq UltraScale EV
250 MHz
Simple scalar

## Slide 32: Optimized Resources: Dedicated Logic
System on Chip
Ethernet
MAC
RAM
Motor
PID
Controller
Sensor
ADC
Sensor
Data
Buffer
Dedicated Logic
Reconfigurable Logic
Matrix Multiplier
Coprocessor
Also see Actel Fusion:http://www.actel.com/products/fusion/default.aspx

## Slide 33
Reconfigurable Architectures
Coarse Grain Reconfigurable Architectures
FPGA Logic Blocks
FPGA Interconnects
Architecture Evaluation Metrics and Models

## Slide 34: FPGA Interconnect
Logics and Interconnects are un-balanced in FPGAs.
Qualitatively:
  “PLDs are 90% routing and 10% logic.”
    Prof. Jonathan Rose, Design of Interconnection Networks for Programmable Logic, Kluwer Academic Publishers, 2004, Page xix;
  “…(in FPGAs) programmable interconnect comes at a substantial cost in area, performance and power.”
    Prof. Jan Rabaey, Digital Integrated Circuits, 2nd Edition, Prentice-Hall, 2003, Page 413;
Quantitatively:
  Area: Logic area v.s. Routing area;
  Delay: Logic delay v.s. Net delay;
  Power: Dynamic power consumption by Logic v.s. by Interconnect.

## Slide 35: Unbalance: Area
Relative weight of routing area and logic area of the 20 largest MCNC benchmark circuits, assuming PTM 90nm CMOS process. Data produced by VPR v5.0.2.

## Slide 36: Unbalance: Delay
Delay breakdown along the critical path for the 20 largest MCNC benchmarks,
assuming PTM 90nm CMOS process. Data produced by VPR v5.0.2.
36

## Slide 37: Unbalance: Power
Note:
Double: The length-2 wires;
Hex: The length-6 wires;
Long: The long wires spanning the whole
chip;
IXbar & OXbar: Crossbar at the input &
output pins of the logic blocks.
Dynamic power breakdown for a real circuit [1], assuming the Xilinx Virtex-II FPGAs
[1] L. Shang, A. Kaviani and K. Bathala, “Dynamic power consumption in Virtex-II FPGA family,” ACM FPGA, 2002.

## Slide 38: A Home-Made FPGA Layout
100um
100um
Four 4-input LUTs
Routing Resources
SB+CB
Programming Circuitry
1mm
1mm
8X8 Tiles
SRAM
CLB &
Local MUX
Switch Box & Connection Box

## Slide 39: Communication: Interconnect & Routing
Need a mechanism to move results of computation around.
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB

## Slide 40: Communication: Interconnect & Routing
Nearest Neighbor:
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB

## Slide 41: Communication: Interconnect & Routing
CLB
Nearest Neighbor:
Segmented:
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB

## Slide 42: Communication: Interconnect & Routing
Nearest Neighbor:
Segmented:
Hierarchical:
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB

## Slide 43: NoC-Based FPGA Interconnects
NoC
FPGA
Tile
FPGA
Tile
FPGA
Tile
FPGA
Tile
FPGA
Tile
FPGA
Tile
The wires required for NoC based FPGA are close to be linear to the array size.
We (hardware engineers) know programming multi-FPGA more than programming multi-core processors.

## Slide 44
Reconfigurable Architectures
Coarse Grain Reconfigurable Architectures
FPGA Logic Blocks
FPGA Interconnects
Architecture Evaluation

## Slide 45: FPGA Architecture Description
An FPGA architecture can be described with high level parameters such as array size, switch block type, etc., in a file called x.arch.
Functional Block

## Slide 46: Routing-Resource Graph (RRG)
Directed graph G(V,E), representing routing resources and their connections.
  V: CLB pins and wires. Each node can be associated with capacity, occupancy, and delay, etc.
  E: Switches. Each edge can be associated with delay, etc.
  Routing tree RTi embedded in G(V,E) fully specifies a net's routing path.
46
Notes: 46

## Slide 47: FPGA Architecture and EDA Exploration Framework
FPGA Architecture File (.arch; .xml)
Placement & Routing
Placement & routing Results (.net)

## Slide 48: VPR Architecture and EDA Exploration Framework
VPR: Versatile Placement and Routing
http://www.eecg.toronto.edu/~vaughn/vpr/vpr.html

## Slide 49: FPGA Verilog-to-Routing Project Experiment Flow
Experiment Flow:
  Tech mapping (ABC)
  Packing using (T-Pack)
  Cluster activity estimation (Odin-2)
  P&R (VPR)
  Power estimation using KPM [15]
    Overestimates, but produces results with good fidelity
    HSPICE simulation delays and model parameters annotated into VPR architecture XML file for delay and power modeling
  Benchmark: MCNC suite
Please refer to Verilog-to-Routing project page
http://code.google.com/p/vtr-verilog-to-routing/
Notes: 49

## Slide 50: Reconfigurable Architecture Research Topics
Logic Blocks
  Use non-LUT type of logic blocks in FPGAs
  Cluster with logic blocks in a way to reduce wiring requirements
Interconnect Networks
  Various ways to organize FPGA wires efficiently
  Switch box design to use minimum area to provide maximum flexibility
Low Power
  Dual Vdd, Dual Vt to reduce leakage power
  Apply power gating to FPGAs
Fault Tolerance and Emerging Technologies for FPGA Architectures

## Slide 51: Reading List This Week
  Rethinking FPGAs: Elude the Flexibility Excess of LUTs with And-Inverter Cones, FPGA 2012, Feb, 2012. (propose not to use LUTs but other basic blocks in FPGAs)
  Analysis and Evaluation of a Hybrid Interconnect Structure for FPGAs, ICCAD 2007. (propose a hybrid interconnect structure to provide the scalability for FPGA wires)
  Defect-Tolerant FPGA Architecture Exploration, FPL 06. (propose a family of defect-tolerant FPGA architectures)
  Assignment: Find 3 recent (in the past 3 years) papers on FPGA architecture research and write in one page for each paper of their identified problems and their solutions. Due in Mar 30, 2022.
Notes: 51