## Slide 1
Prof. Yajun Ha
EE216 Reconfigurable Computing
ShanghaiTech University
Shanghai, China
Topic 15：Accelerating Sobel Filter in SDSoC
Notes: 1

## Slide 2: Sobel Filter Algorithm
The Sobel function Computes the gradients of input image in both x and y direction by convolving the kernel with input image being processed.

## Slide 3: Sobel Filter Code
Load image
Save image
Apply an Sobel Filter
int main(int argc, char** argv)
{
  cv::Mat image, sobel;
  image = cv::imread(argv[1], 0);
  sobel.create(image.rows,image.cols,CV_8UC1);
  sobel.data =(PIXEL*)sds_alloc(sizeof(PIXEL)*image.rows*image.cols);
  jf::sobel(image, sobel);
  cv::imwrite("hw_sobel.jpg", sobel);
  return 0;
}

## Slide 4: Naïve Sobel Filter Implementation
Iterate over an input image
Load image window
Applying 3x3 Sobel filter
Writing to output image
void jf_naive_sobel(PIXEL* src, PIXEL* dst, int rows, int cols)
{
  int row, col;
  PIXEL image_window[3][3];
  for(row = 0; row < rows+1; row++)
  {
    for(col = 0; col < cols+1; col++)
    {
    PIXEL _sobel;
    if(row<=1 || col<=1 || row>(rows-1) || col>(cols-1))
    _sobel = 0;
    else
    {
      for(int i=0; i<3; i++)
      {
        for(int j=0; j<3; j++)
        {
        image_window[i][j] = src[(row+i-1)*cols+(col+j-1)];
        }
      }
      _sobel = sobel3x3_kernel(image_window);
      }
      if(row>1 && col>1)
      dst[(row-1)*cols+(col-1)] = _sobel;
    }
  }
}

## Slide 5: Run the Naïve Sobel on a Zynq Board
1180ms@ 720p, 300MHz

## Slide 6: Problem 1: Non-Sequential Overlapped Memory Access
9 memory access per iteration
void jf_naive_sobel(PIXEL* src, PIXEL* dst, int rows, int cols)
{
  int row, col;
  PIXEL image_window[3][3];
  for(row = 0; row < rows+1; row++)
  {
    for(col = 0; col < cols+1; col++)
    {
    PIXEL _sobel;
    if(row<=1 || col<=1 || row>(rows-1) || col>(cols-1))
    _sobel = 0;
    else
    {
      for(int i=0; i<3; i++)
      {
        for(int j=0; j<3; j++)
        {
        image_window[i][j] = src[(row+i-1)*cols+(col+j-1)];
        }
      }
      _sobel = sobel3x3_kernel(image_window);
      }
      if(row>1 && col>1)
      dst[(row-1)*cols+(col-1)] = _sobel;
    }
  }
}

## Slide 7: Problem 1: Non-Sequential Overlapped Memory
Read 9 pix

## Slide 8: Problem 1: Non-Sequential Overlapped Memory
Read 9 pix

## Slide 9: Problem 1: Non-Sequential Overlapped Memory
Read 9 pix

## Slide 10: Problem 1: Non-Sequential Overlapped Memory
Read 9 pix

## Slide 11: Problem 1: Non-Sequential Overlapped Memory
Read 9 pix
Memory Access: 9 * 48 = 432 pixels
For 720p: 1278*718*9 = 8258436 pixels

## Slide 12: Solution 1: Direct Stream Using Line and Window Buffers
Shift line buffer
Read 1 pix

## Slide 13: Solution 1: Direct Stream Using Line and Window Buffers
Shift line buffer
Read 1 pix

## Slide 14: Solution 1: Direct Stream Using Line and Window Buffers
Shift line buffer
Read 1 pix

## Slide 15: Solution 1: Direct Stream Using Line and Window Buffers
Read 1 pix
Shift line buffer
Processing Window

## Slide 16: Solution 1: Direct Stream Using Line and Window Buffers
Read 1 pix
Shift line buffer
Processing Window

## Slide 17: Solution 1: Direct Stream Using Line and Window Buffers
Memory Access: 1 * 80 = 80 pixels
With 1080p, 2,073,600 pixels (9x less!))
Shift line buffer
Read 1 pix
Processing Window

## Slide 18: Line Buffer and Window Buffer in HLS
static void jFsobel3x3 (
hls::stream<PIXEL>& src,
hls::stream<PIXEL>& dst,
int rows, int cols)
{
  PIXEL _sobel;
  PIXEL LineBuffer[3][WIDTH];
  PIXEL WindowBuffer[3][3];
  ap_uint<13> row, col;
  ap_uint<2> lb_r_i;
  ap_uint<2> top, mid, btm;//linebuffer row index
  for(col = 0; col < cols; col++)
  {
    LineBuffer[0][col] = 0;
    LineBuffer[1][col] = src.read();
  }
Init the line buffer

## Slide 19: Line Buffer and Window Buffer in HLS
lb_r_i = 2;
for(row = 1; row < rows + 1; row++)
{
  if(lb_r_i == 2) top = 0; mid = 1; btm = 2;
  else if(lb_r_i == 0) top = 1; mid = 2; btm = 0;
  else if(lb_r_i == 1) top = 2; mid = 0; btm = 1;
  WindowBuffer[top][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[mid][0] = WindowBuffer[mid][1] = 0;
  WindowBuffer[btm][0] = WindowBuffer[btm][1] = 0;
  for(col = 0; col < cols; col++)
  {
    if(row < rows) LineBuffer[btm][col] = src.read();
    Else LineBuffer[btm][col] = 0;
    WindowBuffer[0][2] = LineBuffer[top][col];
    WindowBuffer[1][2] = LineBuffer[mid][col];
    WindowBuffer[2][2] = LineBuffer[btm][col];
    _sobel = sobel_kernel(WindowBuffer);
    WindowBuffer[0][0] = WindowBuffer[0][1];
    WindowBuffer[1][0] = WindowBuffer[1][1];
    WindowBuffer[2][0] = WindowBuffer[2][1];
    WindowBuffer[0][1] = WindowBuffer[0][2];
    WindowBuffer[1][1] = WindowBuffer[1][2];
    WindowBuffer[2][1] = WindowBuffer[2][2];
    dst.write(_sobel);
  }
  lb_r_i++;
  if(lb_r_i == 3) lb_r_i = 0;
}
Shift the line buffer by rotating the index
Init the window buffer
fill the line buffer
fill the window buffer
Apply dilate operation
update the window buffer
export the result
update the index

## Slide 20: Buffer Initialization
Init the line buffer
image
  for(col = 0; col < cols; col++)
  {
    LineBuffer[0][col] = 0;
    LineBuffer[1][col] = src.read();
  }
  WindowBuffer[top][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[mid][0] = WindowBuffer[mid][1] = 0;
  WindowBuffer[btm][0] = WindowBuffer[btm][1] = 0;
Init the window buffer

## Slide 21: Fill and Update Buffer (1)
  col = 0, top = 0, mid = 1, btm = 2
  for(col = 0; col < cols; col++)
  {
  if(row < rows)
  LineBuffer[btm][col] = src.read();
  Else
  LineBuffer[btm][col] = 0;
fill the line buffer
  top = 0, mid = 1, btm = 2
  WindowBuffer[0][2] = LineBuffer[top][col];
  WindowBuffer[1][2] = LineBuffer[mid][col];
  WindowBuffer[2][2] = LineBuffer[btm][col];
  WindowBuffer[0][0] = WindowBuffer[0][1];
  WindowBuffer[1][0] = WindowBuffer[1][1];
  WindowBuffer[2][0] = WindowBuffer[2][1];
  WindowBuffer[0][1] = WindowBuffer[0][2];
  WindowBuffer[1][1] = WindowBuffer[1][2];
  WindowBuffer[2][1] = WindowBuffer[2][2];
fill the window buffer
  _sobel = sobel_kernel(WindowBuffer);
update the window buffer

## Slide 22
fill the linebuffer
  top = 0, mid = 1, btm = 2
  WindowBuffer[0][2] = LineBuffer[top][col];
  WindowBuffer[1][2] = LineBuffer[mid][col];
  WindowBuffer[2][2] = LineBuffer[btm][col];
  WindowBuffer[0][0] = WindowBuffer[0][1];
  WindowBuffer[1][0] = WindowBuffer[1][1];
  WindowBuffer[2][0] = WindowBuffer[2][1];
  WindowBuffer[0][1] = WindowBuffer[0][2];
  WindowBuffer[1][1] = WindowBuffer[1][2];
  WindowBuffer[2][1] = WindowBuffer[2][2];
fill the windowbuffer
  _sobel = sobel_kernel(WindowBuffer);
update the windowbuffer
  col = 1, top = 0, mid = 1, btm = 2
  for(col = 0; col < cols; col++)
  {
  if(row < rows)
  LineBuffer[btm][col] = src.read();
  Else
  LineBuffer[btm][col] = 0;
Fill and Update Buffer (2)

## Slide 23: Fill and Update Buffer (3)
fill the linebuffer
  top = 1, mid = 2, btm = 0
  WindowBuffer[0][2] = LineBuffer[top][col];
  WindowBuffer[1][2] = LineBuffer[mid][col];
  WindowBuffer[2][2] = LineBuffer[btm][col];
  WindowBuffer[0][0] = WindowBuffer[0][1];
  WindowBuffer[1][0] = WindowBuffer[1][1];
  WindowBuffer[2][0] = WindowBuffer[2][1];
  WindowBuffer[0][1] = WindowBuffer[0][2];
  WindowBuffer[1][1] = WindowBuffer[1][2];
  WindowBuffer[2][1] = WindowBuffer[2][2];
fill the windowbuffer
  _dilate = dilate_kernel(WindowBuffer);
update the windowbuffer
  col = 0, top = 1, mid = 2, btm = 0
  for(col = 0; col < cols; col++)
  {
  if(row < rows)
  LineBuffer[btm][col] = src.read();
  Else
  LineBuffer[btm][col] = 0;

## Slide 24: Run the Solution 1 on a Zynq Board
15.8ms@ 720p, 300MHz
74x SpeedUp

## Slide 25: Problem 2: Loop Iterations Are Sequential
lb_r_i = 2;
for(row = 1; row < rows + 1; row++)
{
  if(lb_r_i == 2) top = 0; mid = 1; btm = 2;
  else if(lb_r_i == 0) top = 1; mid = 2; btm = 0;
  else if(lb_r_i == 1) top = 2; mid = 0; btm = 1;
  WindowBuffer[top][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[mid][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[btm][0] = WindowBuffer[top][1] = 0;
  for(col = 0; col < cols; col++){
    if(row < rows) LineBuffer[btm][col] = src.read();
    Else LineBuffer[btm][col] = 0;
    WindowBuffer[0][2] = LineBuffer[top][col];
    WindowBuffer[1][2] = LineBuffer[mid][col];
    WindowBuffer[2][2] = LineBuffer[btm][col];
    _sobel = sobel3x3_kernel(WindowBuffer);
    WindowBuffer[0][0] = WindowBuffer[0][1];
    WindowBuffer[1][0] = WindowBuffer[1][1];
    WindowBuffer[2][0] = WindowBuffer[2][1];
    WindowBuffer[0][1] = WindowBuffer[0][2];
    WindowBuffer[1][1] = WindowBuffer[1][2];
    WindowBuffer[2][1] = WindowBuffer[2][2];
    dst << _sobel;
  }
  lb_r_i++;
  if(lb_r_i == 3) lb_r_i = 0;
}
Executing sequentially

## Slide 26: Solution 2: Pipeline Loop Iterations
…
5 cycles / loop iteration
5x speedup
Without pipelining
With pipelining

## Slide 27: Solution 2: Pipeline Loop Iterations
lb_r_i = 2;
for(row = 1; row < rows + 1; row++)
{
  if(lb_r_i == 2) top = 0; mid = 1; btm = 2;
  else if(lb_r_i == 0) top = 1; mid = 2; btm = 0;
  else if(lb_r_i == 1) top = 2; mid = 0; btm = 1;
  WindowBuffer[top][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[mid][0] = WindowBuffer[top][1] = 0;
  WindowBuffer[btm][0] = WindowBuffer[top][1] = 0;
  for(col = 0; col < cols; col++){
  #pragma HLS pipeline II=1
    if(row < rows) LineBuffer[btm][col] = src.read();
    Else LineBuffer[btm][col] = 0;
    WindowBuffer[0][2] = LineBuffer[top][col];
    WindowBuffer[1][2] = LineBuffer[mid][col];
    WindowBuffer[2][2] = LineBuffer[btm][col];
    _sobel = sobel3x3_kernel(WindowBuffer);
    WindowBuffer[0][0] = WindowBuffer[0][1];
    WindowBuffer[1][0] = WindowBuffer[1][1];
    WindowBuffer[2][0] = WindowBuffer[2][1];
    WindowBuffer[0][1] = WindowBuffer[0][2];
    WindowBuffer[1][1] = WindowBuffer[1][2];
    WindowBuffer[2][1] = WindowBuffer[2][2];
    dst << _sobel;
  }
  lb_r_i++;
  if(lb_r_i == 3) lb_r_i = 0;
}
Specify pipelining of loop iterations with Initiation Interval = 1

## Slide 28: Solution 2: Pipeline Loop Iterations
static void jFsobel3x3 (
hls::stream<PIXEL>& src,
hls::stream<PIXEL>& dst,
int rows, int cols)
{
  PIXEL _sobel;
  PIXEL LineBuffer[3][WIDTH];
  #pragma HLS ARRAY_PARTITION variable=LineBuffer complete dim=1
  PIXEL WindowBuffer[3][3];
  #pragma HLS ARRAY_PARTITION variable=WindowBuffer complete dim=0
  ap_uint<13> row, col;
  ap_uint<2> lb_r_i;
  ap_uint<2> top, mid, btm;//linebuffer row index
  for(col = 0; col < cols; col++)
  {
    #pragma HLS pipeline
    LineBuffer[0][col] = 0;
    gray >> LineBuffer[1][col];
  }
The window buffer should provides 9 pixels per cycle, thus the windowbuffer has to be unrolled completely
The linebuffer should provides 3 pixels per cycle, thus expand the array in dimension 1 will be ok

## Slide 29: Run the Solution 1 on a Zynq board
3.7ms@ 720p, 300MHz
4.2x SpeedUp

## Slide 30: Summary
 | latency
A naïve Sobel filter implementation | 1181ms
Problem 1: Non-sequential overlapped memory accesses Solution 1: Reducing memory access by 9x using line and window buffers | 15.8ms
Problem 2: Sequential loop iteration Solution 2: Pipeline loop iteration using the pipeline pragma | 3.7ms
319x Speedup